## Slide 1: Photochemical Modeling of Louisiana for the 2008 Ozone Standard
Chris Emery
ENVIRON International Corporation, Novato CA
November 14, 2012

## Slide 2: Modeling System
Follows from previous SIP modeling effort
  Consistency, familiarity with past LDEQ datasets
  Utilize some new state-of-the-science models
  Adhere to latest EPA requirements and guidance
Photochemical Model: CAMx
Meteorological Model: WRF (new)
Louisiana Emissions Processing
  Stationary: EPS3
  On-road mobile: CONCEPT/MOVES (new)
  Non-road mobile: NONROAD
  Biogenic: MEGAN (new)
Attainment Demonstration: MATS

## Slide 3: Modeling Period
Model one season (September-October 2010)
  EPA guidance is moving away from “episodic” modeling
  Local ozone frequency/magnitude peaks in Spring and Fall
Evaluated statewide 2008-2011 monitoring data
  Tally days exceeding thresholds: 60, 65, 70, 75 ppb
  Look for periods with statewide exceedances
  Identify appropriate “representative” ozone season
    No extremes: 2008 very low, 2011 very high
    Economic/natural deviations: 2009 hit hardest by recession
    Availability of national/regional/local datasets

## Slide 4: Site-Days Exceeding 75 ppb Statewide and By Region

## Slide 5: 2010 Exceedance Analysis

## Slide 6: Modeling Domain
Move to align with national CONUS domain
  Established by Regional Planning Organizations
  Used by EPA for many national modeling analyses
  TCEQ and other CENSARA states are moving to this domain
  Improves data sharing and consistency
Three-grid system
  36 km CONUS
  12 km south-central US
  4 km Louisiana

## Slide 8: Meteorological Modeling
Weather Research and Forecasting Model (WRF)
  Developed/maintained by the National Center for Atmospheric Research (NCAR)
  Used by EPA and many states to support AQ modeling
Run with configuration/options that work best from our recent experience
  Modeling performed by Alpine Geophysics
Model evaluation against observational data
  Statistics for winds, temperature, humidity
  Quantitatively/graphically evaluate precipitation
Interface with CAMx (WRFCAMx)

## Slide 9: Anthropogenic Emissions Processing
LA stationary (EPS3)
  2010 Point sources from LDEQ EIS and hourly ARP/CAMD (ERG)
  Parish-level area sources from 2008 NEI – no change to 2010 (ERG)
LA on-road mobile (CONCEPT)
  Parish-level activity data (HPMS), fuels, fleet mix
  Vehicle emission factors (MOVES)
LA non-road mobile (NMIM/NONROAD)
  Parish-level EPA default equipment/activity
LA Other (EPS3)
  Gulf-wide shipping and O&G (ERG/BOEM)
  Haynesville Shale development (past ENVIRON work for Texas)
  Port Fourchon activity (LSU/Starcrest)
  LA deep-draft shipping ports/lanes (past ENVIRON work, BOEM)
US-wide (SMOKE)
  Processed by Alpine Geophysics
Biogenic (MEGAN)
Daily fires (NCAR FINN)

## Slide 10: Model Performance Evaluation
Evaluate model fidelity for ozone and precursors
  Rely on routine AQS and PAMS monitoring
  Screening model performance
    Basic graphics/statistics evaluating ozone
  Refined model performance
    Expand to precursors
    Conduct diagnostic & sensitivity tests (Probing Tools?)
Identify best model configuration suitable for ozone attainment demonstration
  Avoid “tuning” or curve-fitting
  Any changes must be justifiable, reviewed, documented

## Slide 11: Future Year Modeling
2017 attainment year (Moderate Area)
  Substitute 2010 emissions with 2017 projections
  Reflects controls and forecasted economic changes
  Biogenic emissions remain constant
Nationally (mobile fleet regs, cross-state rule, MACT)
  RPOs & EPA have/developing projections to 2015-2020
Locally
  On/non-road projected per activity forecasts and MOVES/NONROAD
  Phase-in any local rules on stationary sources
  New facilities, closures/shut-downs
  O&G development trends/forecasts
Sensitivity tests for source attribution and control response

## Slide 12: Ozone Attainment Demonstration
EPA Model Attainment Test Software (MATS)
  Ingest 2010 and 2017 CAMx ozone estimates
  Calculate modeled 2017-2010 change as a “relative response factor” (RRF)
    Use RRF to project 2010 design values (DV) at each monitor to 2017
    2010 DV is 5-year weighted average over 2008-2012
  2017 DV must be <75 ppb at all sites
If attainment is not demonstrated:
  Perform “weight of evidence” analyses, or
  Conduct additional local control scenario simulations
    LDEQ to develop packages of potential reductions